You can absolutely combine a hot‑wire anemometer (MAF sensor) with a pitot‑tube + Magnehelic® (or equivalent differential‑pressure gauge) to get the best of both worlds:

## 1. What Each Sensor Brings
Sensor	Measures	Pros	Cons
Pitot + Magnehelic	Air velocity → ΔP (static vs. total)	Very rugged; simple analog readout; low cost (≈$60–80)	Only gives pressure drop; must compute flow and correct for temperature/density
Hot‑Wire Anemometer (MAF)	Mass‐flow rate directly (g/s or SLPM)	Direct mass‐flow (no T&P correction); high bandwidth	Requires clean air (sensitive to contamination); a bit more expensive ($50–$100 used)

Combining them lets you:
1. Cross‑Validate: Spot calibration drift in the hot‑wire by comparing against ΔP‑derived flow.
2. Expand Range: Pitot+Magnehelic excels at high‐velocity ΔP; hot‑wire is more sensitive at low flows.
3. Redundancy & Diagnostics: A sudden divergence (e.g. MAF reads high but ΔP stays low) flags sensor fouling or bypass leaks.

## 2. Typical “Domestic” Hot‑Wire MAF Sources
- Bosch 0 280 217 116
  - Common on GM 4‑cyl engines (’90s–’00s).
  - Measures 0–200 g/s with ~±2% accuracy.
  - Approximate eBay price: $50–$80 used; $120–$150 new.
- Delphi or VDO equivalents
  - Often cross‑reference to Bosch OEM.
  - Similar specs; $60–$90 refurbed on parts sites.
Note: The sensor must be mounted in a straight run of duct at least 4× its length upstream and 2× downstream to avoid flow distortions.

## 3. Integrating Both in Your Filter Box
1. Pitot + Magnehelic Setup
  1. Drill two ⅛″ ports across the combined exit of your filter manifold.
  2. Connect to a 0–1 in w.g. Magnehelic® (e.g. Dwyer 2000 series).
  3. Calibrate at known fan speeds to map ΔP → CFM.
2. MAF (Hot‑Wire) Installation
  1. Insert the Bosch hot‑wire element into a tee‑fitting in the blower inlet plenum (downstream of the filters).
  2. Wire its 4‑ or 5‑pin connector to a small 12 VDC supply + signal ground + signal line.
  3. Use an Arduino or 0–5 V analog‑input PLC to read the output voltage (typically 0.5–4.5 V ∝ mass flow).
3. Data Fusion & Alerts
  1. In your controller (e.g. Node‑RED, PLC), compute:
    1. Flow₁(ΔP) = K·√ΔP (where K is your calibration constant)
    2. Flow₂(MAF) = m·Vout + b (from Bosch calibration curve)
  2. If |Flow₁–Flow₂| > 10% → flag a “sensor fault” or “filter bypass.”
  3. Log both streams so you can detect gradual drift (e.g. MAF contamination).

## 4. Cost & Sourcing Summary
Component	Estimated Unit Cost	Source
Bosch MAF Sensor (0 280 217 116)	$60 (used)	eBay, RockAuto
Magnehelic® Gauge (0–1 in w.g.)	$60	OmegaEngineering, Grainger
Pitot Tube Kit (¼″ brass)	$15	McMaster‑Carr
Arduino Nano or PLC I/O	$10–30	Amazon, AutomationDirect
Wiring & Fittings	$20	Local hardware or HVAC supplier

## 5. Academic & Industry References
- R. J. Goldstein, Fluid Mechanics Measurements, 3rd Ed., Taylor & Francis (2015): overview of pitot and hot‑wire techniques.
- Dwyer Instruments, “Magnehelic® 2000 Series Instruction Manual” (2010).
- SAE Paper 2019‑01‑1052, “Comparison of Hot‑Wire and Pitot‐Tube Air‑Flow Sensors in Automotive Intake Systems” (2019).

### Next Steps
1. Pilot Installation: Mount both sensors in your existing 18×18 manifold.
2. Calibration Runs: Use a known fan curve or blower data to derive K (for ΔP→CFM) and linear coefficients for the Bosch’s Vout→g/s.
3. Integration: Wire into your chosen controller, set thresholds, and begin data logging.
Let me know if you’d like detailed calibration procedures or sample Arduino code to read the Bosch MAF!